## Slide 1
Computer Aided Drawing
INTRODUCTION TO
COMPUTER AIDED DRAWING
KULLIYYAH OF ENGINEERING
INTERNATIONAL ISLAMIC UNIVERSITY MALAYSIA

## Slide 2: OUTLINE
Introduction to CAD
Scales & lines
Geometrical Dimension & Tolerance (GD&T)

## Slide 3: 1. INTRODUCTION TO CAD

## Slide 4: INTRODUCTION TO ENGINEERING DRAWING / CAD
CAD serves as an aid to shape and communicate an abstract idea in your imagination into a 3D or 2D model for others to understand.
CAD enables the development, modification, and optimization of the design process.
CAD enables the development, modification, and optimization of the design process.
Engineers can make more accurate representations and modify them easily to improve design quality.

## Slide 5: CREATE A DRAWING : Using a computer
Usually made by commercial software such as SolidWorks, Catia, AutoCaD, Alibre etc.
2D Drawing
Solid Modeling

## Slide 6: PLANNING YOUR SKETCH
When laying out a drawing sheet, you will need to consider:
The size and scale of the object you will show the sheet size.
The measurement system (units) for the drawing.
The space necessary for standard notes and title block.
Note: The object you are drawing is the “star” of the sketch. Keep the object near the center of the sheet. It should be boldly drawn, using thick visible lines. Make it large enough to fill most of the sheet so that the details are clearly visible.

## Slide 7: 2. SCALES & LINES

## Slide 8: ENGINEERING DRAWING BASICS: Drawing Scale
Designation of a scale consists of the word “SCALE” followed by the indication of its ratio as follows:
  SCALE 1:1 for full size
  SCALE X:1 for enlargement scales (i.e. X > 1)
  SCALE 1:X for reduction scales (i.e. X< 1)
SCALE 1 : 2
Drawing scale is the reduction or enlargement of the drawn object relative to the real object
Real Measurement
Drawing

## Slide 9: ENGINEERING DRAWING BASICS: Drawing Scale
- Shape
Space between letters
Space between words
Legibility/clarity
- Size (or text height) - line thickness
Uniformity
Text’s style on the drawing must have the following 2 properties
Examples
GOOD
Not uniform in style.
Not uniform in height.
Not uniformly vertical.
Not uniform in
thickness of stroke.
Inappropriate space
between letters

## Slide 10: MEANING AND TYPES OF BASIC LINES
Visible line: represent features that can be seen in the current view.
Dimension line, Extension line & Leader line: indicate the sizes and location of features.
Hidden line: represent features that can not be seen in the current view.
Center line: represents symmetry, path of motion, centers of circles, axis of axisymmetrical parts
Thickness Style | Thick | Thin
Continuous |  | 
Dash |  | 
Chain |  | 
Visible line
1. Dimension line
2. Extension line
3. Leader line
Center line
Hidden line

## Slide 11: TYPES OF LINES

## Slide 12: EXAMPLE :

## Slide 13: ENGINEERING DRAWING BASICS : Dimensioning
Dimensioning is the process of specifying part’s information by using of lines, number, symbols and notes.

## Slide 14
DIMENSIONING COMPONENTS
Extension lines
indicate the location on the object’s features that are dimensioned.
Dimension lines (with arrowheads)
indicate the direction and extent of a dimension, and inscribe dimension numbers.
Dimension numbers (or dimension figures)
Leader lines
indicate details of the feature with a local note.
Notes
local or general notes.
20
13
123o
f10
R16
Example

## Slide 15: DIMENSIONING ~ Recommended Practice ~

## Slide 16: ENGINEERING DRAWING BASIC DIMENSIONING

## Slide 17
EXTENSION LINE
Always leave a visible gap (≈ 1 mm) from a view or center lines before start drawing a line.
Extend the lines beyond the (last) dimension line 2-3 mm.
Good practice
1
2
3
2
4
Poor practice

## Slide 18
Do not break the extension lines as they cross any line types, e.g. visible line, hidden line or center line, i.e. extension line always a continuous line.
Good practice
Poor practice
1
2
3
EXTENSION LINE

## Slide 19
Good practice
Dimension lines should be appropriately spaced apart from each other and the view.
25
34
At least 2 times
of a font size
30
At least 1 time
of a font size
25
34
30
25
34
30
Too close
Too far
DIMENSION LINE
Poor practice

## Slide 20
The height of numbers is suggested to be 2.5~3 mm.
Place the numbers at about 1 mm above and at a middle of a
dimension line (for ISO dimensioning).
DIMENSION NUMBER : General
Good practice
25
34
25
34
30
30
Poor practice

## Slide 21: 3. GEOMETRICAL DIMENSION & TOLERANCE (GD&T)

## Slide 22
Geometrical Dimension and Tolerance

## Slide 23
Geometrical Dimension and Tolerance

## Slide 24
Geometrical Dimension and Tolerance

## Slide 25
Geometrical Dimension and Tolerance

## Slide 26
Geometrical Dimension and Tolerance

## Slide 27
Geometrical Dimension and Tolerance

## Slide 28
Geometrical Dimension and Tolerance

## Slide 29
Geometrical Dimension and Tolerance

## Slide 30
Geometrical Dimension and Tolerance

## Slide 31
Thank You