## Slide 1: William Stallings Computer Organization and Architecture 10th Edition
Notes: Lecture slides prepared for “Computer Organization and Architecture”, 10/e, by William Stallings, Chapter 20 “Control Unit Operation”.

## Slide 2: Chapter 20
Control Unit Operation
Notes: In Chapter 12, we pointed out that a machine instruction set goes a long way toward
defining the processor. If we know the machine instruction set, including an understanding
of the effect of each opcode and an understanding of the addressing modes,
and if we know the set of user- visible registers, then we know the functions that the
processor must perform. This is not the complete picture. We must know the external
interfaces, usually through a bus, and how interrupts are handled. With this line
of reasoning, the following list of those things needed to specify the function of a
processor emerges:
1. Operations (opcodes)
2. Addressing modes
3. Registers
4. I/O module interface
5. Memory module interface
6. Interrupts
This list, though general, is rather complete. Items 1 through 3 are defined by the
instruction set. Items 4 and 5 are typically defined by specifying the system bus.
Item 6 is defined partially by the system bus and partially by the type of support the
processor offers to the operating system.
This list of six items might be termed the functional requirements for a processor.
They determine what a processor must do. This is what occupied us in Parts
Two and Four. Now, we turn to the question of how these functions are performed
or, more specifically, how the various elements of the processor are controlled to
provide these functions. Thus, we turn to a discussion of the control unit, which
controls the operation of the processor.

## Slide 3: Micro-Operations
The functional, or atomic, operations of a processor
Series of steps, each of which involves the processor registers
Micro refers to the fact that each step is very simple and accomplishes very little
The execution of a program consists of the sequential execution of instructions
  Each instruction is executed during an instruction cycle made up of shorter subcycles (fetch, indirect, execute, interrupt)
  The execution of each subcycle involves one or more shorter operations (micro-operations)
Notes: We have seen that the operation of a computer, in executing a program, consists of a
sequence of instruction cycles, with one machine instruction per cycle. Of course, we
must remember that this sequence of instruction cycles is not necessarily the same
as the written sequence of instructions that make up the program, because of the
existence of branching instructions. What we are referring to here is the execution
time sequence of instructions.
We have further seen that each instruction cycle is made up of a number of
smaller units. One subdivision that we found convenient is fetch, indirect, execute,
and interrupt, with only fetch and execute cycles always occurring.
To design a control unit, however, we need to break down the description
further. In our discussion of pipelining in Chapter 14, we began to see that a further
decomposition is possible. In fact, we will see that each of the smaller cycles
involves a series of steps, each of which involves the processor registers. We will
refer to these steps as micro-operations . The prefix micro refers to the fact that each
step is very simple and accomplishes very little,
Micro-operations are the functional, or atomic, operations of a processor. In this
section, we will examine micro-operations to gain an understanding of how the events
of any instruction cycle can be described as a sequence of such micro-operations.
A simple example will be used. In the remainder of this chapter, we then show how the
concept of micro-operations serves as a guide to the design of the control unit.

## Slide 4
Notes: Figure 20.1 depicts the relationship
among the various concepts we have been discussing. To summarize, the execution
of a program consists of the sequential execution of instructions. Each instruction
is executed during an instruction cycle made up of shorter subcycles (e.g., fetch,
indirect, execute, interrupt). The execution of each subcycle involves one or more
shorter operations, that is, micro-
operations.

## Slide 5: The Fetch Cycle
Occurs at the beginning of each instruction cycle and causes an instruction to be fetched from memory
Four registers are involved:
  Memory Address Register (MAR)
    Connected to address bus
    Specifies address for read or write operation
  Memory Buffer Register (MBR)
    Connected to data bus
    Holds data to write or last data read
  Program Counter (PC)
    Holds address of next instruction to be fetched
  Instruction Register (IR)
    Holds last instruction fetched
Notes: We begin by looking at the fetch cycle, which occurs at the beginning of each instruction
cycle and causes an instruction to be fetched from memory. For purposes of
discussion, we assume the organization depicted in Figure 14.6 (Data Flow , Fetch
Cycle ). Four registers are involved:
■ Memory address register (MAR): Is connected to the address lines of the system
bus. It specifies the address in memory for a read or write operation.
■ Memory buffer register (MBR): Is connected to the data lines of the system bus.
It contains the value to be stored in memory or the last value read from memory.
■ Program counter (PC): Holds the address of the next instruction to be
fetched.
■ Instruction register (IR): Holds the last instruction fetched.

## Slide 6
Notes: Let us look at the sequence of events for the fetch cycle from the point of view
of its effect on the processor registers. An example appears in Figure 20.2. At the
beginning of the fetch cycle, the address of the next instruction to be executed is in
the program counter (PC); in this case, the address is 1100100. The first step is to
move that address to the memory address register (MAR) because this is the only
register connected to the address lines of the system bus. The second step is to bring
in the instruction. The desired address (in the MAR) is placed on the address bus,
the control unit issues a READ command on the control bus, and the result appears
on the data bus and is copied into the memory buffer register (MBR). We also need
to increment the PC by the instruction length to get ready for the next instruction.
Because these two actions (read word from memory, increment PC) do not interfere
with each other, we can do them simultaneously to save time. The third step is
to move the contents of the MBR to the instruction register (IR). This frees up the
MBR for use during a possible indirect cycle.
Thus, the simple fetch cycle actually consists of three steps and four micro-operations.
Each micro-operation involves the movement of data into or out of a
register. So long as these movements do not interfere with one another, several of
them can take place during one step, saving time.

## Slide 7: Rules for Micro-Operations Grouping
Proper sequence must be followed
  MAR  (PC) must precede MBR  (memory)
Conflicts must be avoided
  Must not read and write same register at same time
  MBR  (memory) and IR  (MBR) must not be in same cycle
One of the micro-operations involves an addition
  To avoid duplication of circuitry, this addition could be performed by the ALU
  The use of the ALU may involve additional micro-operations, depending on the functionality of the ALU and the organization of the processor
Notes: The groupings of micro-operations must follow two simple rules:
1. The proper sequence of events must be followed. Thus (MAR  (PC)) must
precede (MBR  Memory) because the memory read operation makes use of
the address in the MAR.
2. Conflicts must be avoided. One should not attempt to read to and write from
the same register in one time unit, because the results would be unpredictable.
For example, the micro-operations (MBR  Memory) and (IR  MBR)
should not occur during the same time unit.
A final point worth noting is that one of the micro-operations
involves an addition. To avoid duplication of circuitry, this addition could be performed by
the ALU. The use of the ALU may involve additional micro-operations,
depending on the functionality of the ALU and the organization of the processor. We defer a
discussion of this point until later in this chapter.
It is useful to compare events described in this and the following subsections to
Figure 3.5 (Example of Program Execution ). Whereas micro-operations
are ignored in that figure, this discussion shows the micro-operations
needed to perform the subcycles of the instruction cycle.

## Slide 8: Indirect Cycle
Once an instruction is fetched, the next step is to fetch source operands
Assuming a one-address instruction format, with direct and indirect addressing allowed:
  If the instruction specifies an indirect address, then an indirect cycle must precede the execute cycle
  The address field of the instruction is transferred to the MAR
  This is then used to fetch the address of the operand
  Finally, the address field of the IR is updated from the MBR, so that it now contains a direct rather than an indirect address
  The IR is now in the same state as if indirect addressing had not been used, and it is ready for the execute cycle
Notes: Once an instruction is fetched, the next step is to fetch source operands. Continuing our
simple example, let us assume a one-address instruction format, with direct and indirect
addressing allowed. If the instruction specifies an indirect address, then an indirect cycle
must precede the execute cycle. The data flow differs somewhat from that indicated in
Figure 14.7 (Data Flow , Indirect Cycle ) and includes the following micro-operations:
t1: MAR  (IR(Address))
t2: MBR  Memory
t3: IR(Address)  (MBR(Address))
The address field of the instruction is transferred to the MAR. This is then used
to fetch the address of the operand. Finally, the address field of the IR is updated
from the MBR, so that it now contains a direct rather than an indirect address.
The IR is now in the same state as if indirect addressing had not been used,
and it is ready for the execute cycle. We skip that cycle for a moment, to consider
the interrupt cycle.

## Slide 9: Interrupt Cycle
At the completion of the execute cycle, a test is made to determine whether any enabled interrupts have occurred, and if so, the interrupt cycle occurs
The nature of this cycle varies greatly from one machine to another
In a simple sequence of events:
  In the first step the contents of the PC are transferred to the MBR so that they can be saved for return from the interrupt
  Then the MAR is loaded with the address at which the contents of the PC are to be saved, and the PC is loaded with the address of the start of the interrupt-processing routine
    These two actions may each be a single micro-operation
    Because most processors provide multiple types and/or levels of interrupts, it may take one or more additional micro-operations to obtain the Save_Address and the Routine_Address before they can be transferred to the MAR and PC respectively
  Once this is done, the final step is to store the MBR, which contains the old value of the PC, into memory
  The processor is now ready to begin the next instruction cycle
Notes: At the completion of the execute cycle, a test is made to determine whether any
enabled interrupts have occurred. If so, the interrupt cycle occurs. The nature of this
cycle varies greatly from one machine to another. We present a very simple sequence
of events, as illustrated in Figure 14.8 (Data Flow, Indirect Cycle ). We have
t1: MBR  (PC)
t2: MAR  Save_Address
PC  Routine_Address
t3: Memory  (MBR)
In the first step, the contents of the PC are transferred to the MBR, so that
they can be saved for return from the interrupt. Then the MAR is loaded with
the address at which the contents of the PC are to be saved, and the PC is loaded
with the address of the start of the interrupt-processing routine. These two actions
may each be a single micro-operation. However, because most processors provide
multiple types and/or levels of interrupts, it may take one or more additional micro-
operations to obtain the Save_Address and the Routine_Address before they can
be transferred to the MAR and PC, respectively. In any case, once this is done, the
final step is to store the MBR, which contains the old value of the PC, into memory.
The processor is now ready to begin the next instruction cycle.

## Slide 10: Execute Cycle
Because of the variety of opcodes, there are a number of different sequences of micro-operations that can occur
Instruction decoding
  The control unit examines the opcode and generates a sequence of micro-operations based on the value of the opcode
A simplified add instruction:
  ADD R1, X (which adds the contents of the location X to register R1)
    In the first step the address portion of the IR is loaded into the MAR
    Then the referenced memory location is read
    Finally the contents of R1 and MBR are added by the ALU
    Additional micro-operations may be required to extract the register reference from the IR and perhaps to stage the ALU inputs or outputs in some intermediate registers
Notes: The fetch, indirect, and interrupt cycles are simple and predictable. Each involves
a small, fixed sequence of micro-operations and, in each case, the same micro-operations
are repeated each time around.
This is not true of the execute cycle. Because of the variety of opcodes, there
are a number of different sequences of micro-operations that can occur. The control
unit examines the opcode and generates a sequence of micro-operations based on
the value of the opcode. This is referred to as instruction decoding.
Let us consider several hypothetical examples.
First, consider an add instruction:
ADD R1, X
which adds the contents of the location X to register R1. The following sequence of
Micro-operations might occur:
t1: MAR  (IR(address))
t2: MBR  Memory
t3: R1  (R1) + (MBR)
We begin with the IR containing the ADD instruction. In the first step, the
address portion of the IR is loaded into the MAR. Then the referenced memory
location is read. Finally, the contents of R1 and MBR are added by the ALU. Again,
this is a simplified example. Additional micro-operations may be required to extract
the register reference from the IR and perhaps to stage the ALU inputs or outputs
in some intermediate registers.

## Slide 11
Notes: We have seen that each phase of the instruction cycle can be decomposed into a
sequence of elementary micro-operations. In our example, there is one sequence
each for the fetch, indirect, and interrupt cycles, and, for the execute cycle, there is
one sequence of micro-operations for each opcode.
To complete the picture, we need to tie sequences of micro-operations
together, and this is done in Figure 20.3. We assume a new 2-bit register called the
instruction cycle code (ICC). The ICC designates the state of the processor in terms
of which portion of the cycle it is in:
00: Fetch
01: Indirect
10: Execute
11: Interrupt
At the end of each of the four cycles, the ICC is set appropriately. The indirect
cycle is always followed by the execute cycle. The interrupt cycle is always followed
by the fetch cycle (see Figure 14.4, The Instruction Cycle ). For both the fetch and
execute cycles, the next cycle depends on the state of the system.
Thus, the flowchart of Figure 20.3 defines the complete sequence of micro-operations,
depending only on the instruction sequence and the interrupt pattern.
Of course, this is a simplified example. The flowchart for an actual processor would
be more complex. In any case, we have reached the point in our discussion in which
the operation of the processor is defined as the performance of a sequence of micro-
operations.
We can now consider how the control unit causes this sequence to occur.

## Slide 12: Control Unit Functional Requirements
By reducing the operation of the processor to its most fundamental level we are able to define exactly what it is that the control unit must cause to happen
Three step process to lead to a characterization of the control unit:
  Define basic elements of processor
  Describe micro-operations processor performs
  Determine the functions that the control unit must perform to cause the micro-operations to be performed
The control unit performs two basic tasks:
  Sequencing
  Execution
Notes: As a result of our analysis in the preceding section, we have decomposed the behavior
or functioning of the processor into elementary operations, called micro-
operations. By reducing the operation of the processor to its most fundamental level, we are
able to define exactly what it is that the control unit must cause to happen. Thus, we
can define the functional requirements for the control unit: those functions that the
control unit must perform. A definition of these functional requirements is the basis
for the design and implementation of the control unit.
With the information at hand, the following three-step process leads to a characterization
of the control unit:
1. Define the basic elements of the processor.
2. Describe the micro-operations that the processor performs.
Determine the functions that the control unit must perform to cause the micro-operations
to be performed.
We have already performed steps 1 and 2. Let us summarize the results. First,
the basic functional elements of the processor are the following:
■ ALU
■ Registers
■ Internal data paths
■ External data paths
■ Control unit
Some thought should convince you that this is a complete list. The ALU is the
functional essence of the computer. Registers are used to store data internal to the
processor. Some registers contain status information needed to manage instruction
sequencing (e.g., a program status word). Others contain data that go to or come
from the ALU, memory, and I/O modules. Internal data paths are used to move
data between registers and between register and ALU. External data paths link
registers to memory and I/O modules, often by means of a system bus. The control
unit causes operations to happen within the processor.
The execution of a program consists of operations involving these processor
elements. As we have seen, these operations consist of a sequence of
micro-operations. Upon review of Section 20.1, the reader should see that all micro-operations
fall into one of the following categories:
■ Transfer data from one register to another.
■ Transfer data from a register to an external interface (e.g., system bus).
■ Transfer data from an external interface to a register.
■ Perform an arithmetic or logic operation, using registers for input and output.
All of the micro-operations needed to perform one instruction cycle, including all
of the micro-operations to execute every instruction in the instruction set, fall into
one of these categories.
We can now be somewhat more explicit about the way in which the control
unit functions. The control unit performs two basic tasks:
■ Sequencing: The control unit causes the processor to step through a series
of micro-operations in the proper sequence, based on the program being executed.
■ Execution: The control unit causes each micro-operation to be performed.
The preceding is a functional description of what the control unit does. The
key to how the control unit operates is the use of control signals.

## Slide 13
Notes: We have defined the elements that make up the processor (ALU, registers, data
paths) and the micro-operations that are performed. For the control unit to perform
its function, it must have inputs that allow it to determine the state of the system and
outputs that allow it to control the behavior of the system. These are the external
specifications of the control unit. Internally, the control unit must have the logic
required to perform its sequencing and execution functions. We defer a discussion
of the internal operation of the control unit to Section 20.3 and Chapter 21. The
remainder of this section is concerned with the interaction between the control unit
and the other elements of the processor.
Figure 20.4 is a general model of the control unit, showing all of its inputs and
outputs. The inputs are:
■ Clock: This is how the control unit “keeps time.” The control unit causes one
micro-operation (or a set of simultaneous micro-operations) to be performed
for each clock pulse. This is sometimes referred to as the processor cycle time,
or the clock cycle time.
■ Instruction register: The opcode and addressing mode of the current instruction
are used to determine which micro-operations to perform during the execute cycle.
■ Flags: These are needed by the control unit to determine the status of the
processor and the outcome of previous ALU operations. For example, for the
Increment-and-skip-if-zero (ISZ) instruction, the control unit will increment
the PC if the zero flag is set.
■ Control signals from control bus: The control bus portion of the system bus
provides signals to the control unit.
The outputs are as follows:
■ Control signals within the processor: These are two types: those that cause
data to be moved from one register to another, and those that activate specific
ALU functions.
■ Control signals to control bus: These are also of two types: control signals to
memory, and control signals to the I/O modules.
Three types of control signals are used: those that activate an ALU function;
those that activate a data path; and those that are signals on the external system bus
or other external interface. All of these signals are ultimately applied directly as
binary inputs to individual logic gates.
Let us consider again the fetch cycle to see how the control unit maintains
control. The control unit keeps track of where it is in the instruction cycle. At a
given point, it knows that the fetch cycle is to be performed next. The first step is to
transfer the contents of the PC to the MAR. The control unit does this by activating
the control signal that opens the gates between the bits of the PC and the bits of
the MAR. The next step is to read a word from memory into the MBR and increment
the PC. The control unit does this by sending the following control signals
simultaneously:
■ A control signal that opens gates, allowing the contents of the MAR onto the
address bus;
■ A memory read control signal on the control bus;
■ A control signal that opens the gates, allowing the contents of the data bus to
be stored in the MBR;
■ Control signals to logic that add 1 to the contents of the PC and store the
result back to the PC.
Following this, the control unit sends a control signal that opens gates between the
MBR and the IR.
This completes the fetch cycle except for one thing: The control unit must
decide whether to perform an indirect cycle or an execute cycle next. To decide this,
it examines the IR to see if an indirect memory reference is made.
The indirect and interrupt cycles work similarly. For the execute cycle, the
control unit begins by examining the opcode and, on the basis of that, decides which
sequence of micro-operations to perform for the execute cycle.

## Slide 14
Notes: To illustrate the functioning of the control unit, let us examine a simple example.
Figure 20.5 illustrates the example. This is a simple processor with a single accumulator
(AC). The data paths between elements are indicated. The control paths
for signals emanating from the control unit are not shown, but the terminations of
control signals are labeled Ci and indicated by a circle. The control unit receives
inputs from the clock, the IR, and flags. With each clock cycle, the control unit
reads all of its inputs and emits a set of control signals. Control signals go to three
separate destinations:
■ Data paths: The control unit controls the internal flow of data. For example, on
instruction fetch, the contents of the memory buffer register are transferred to
the IR. For each path to be controlled, there is a switch (indicated by a circle in
the figure). A control signal from the control unit temporarily opens the gate
to let data pass.
■ ALU: The control unit controls the operation of the ALU by a set of control
signals. These signals activate various logic circuits and gates within the ALU.
■ System bus: The control unit sends control signals out onto the control lines of
the system bus (e.g., memory READ).

## Slide 15
(Table can be found on page 719 in the textbook.)
Notes: The control unit must maintain knowledge of where it is in the instruction
cycle. Using this knowledge, and by reading all of its inputs, the control unit emits
a sequence of control signals that causes micro-operations to occur. It uses the
clock pulses to time the sequence of events, allowing time between events for signal
levels to stabilize. Table 20.1 indicates the control signals that are needed for
some of the micro-operation sequences described earlier. For simplicity, the data
and control paths for incrementing the PC and for loading the fixed addresses into
the PC and MAR are not shown.
It is worth pondering the minimal nature of the control unit. The control unit
is the engine that runs the entire computer. It does this based only on knowing the
instructions to be executed and the nature of the results of arithmetic and logical
operations (e.g., positive, overflow, etc.). It never gets to see the data being processed
or the actual results produced. And it controls everything with a few control
signals to points within the processor and a few control signals to the system bus.

## Slide 16
Notes: Figure 20.5 indicates the use of a variety of data paths. The complexity of this type of
organization should be clear. More typically, some sort of internal bus arrangement,
as was suggested in Figure 14.2 (Internal Structure of the CPU ), will be used.
Using an internal processor bus, Figure 20.5 can be rearranged as shown in
Figure 20.6. A single internal bus connects the ALU and all processor registers.
Gates and control signals are provided for movement of data onto and off the bus
from each register. Additional control signals control data transfer to and from the
system (external) bus and the operation of the ALU.
Two new registers, labeled Y and Z, have been added to the organization.
These are needed for the proper operation of the ALU. When an operation involving
two operands is performed, one can be obtained from the internal bus, but the
other must be obtained from another source. The AC could be used for this purpose,
but this limits the flexibility of the system and would not work with a processor
with multiple general-purpose registers. Register Y provides temporary storage
for the other input. The ALU is a combinatorial circuit (see Chapter 11) with no
internal storage. Thus, when control signals activate an ALU function, the input to
the ALU is transformed to the output. Therefore, the output of the ALU cannot
be directly connected to the bus, because this output would feed back to the input.
Register Z provides temporary output storage.

## Slide 17
Notes: To illustrate some of the concepts introduced thus far in this chapter, let us consider
the Intel 8085. Its organization is shown in Figure 20.7. Several key components that
may not be self-explanatory are:
■ Incrementer/decrementer address latch: Logic that can add 1 to or subtract 1
from the contents of the stack pointer or program counter. This saves time by
avoiding the use of the ALU for this purpose.
■ Interrupt control: This module handles multiple levels of interrupt signals.
■ Serial I/O control: This module interfaces to devices that communicate 1 bit
at a time.

## Slide 18
Table 20.2
Intel
8085 External Signals (page 1 of 2)
(Table can be found on page 722 in the textbook.)
Notes: Table 20.2 describes the external signals into and out of the 8085. These are
linked to the external system bus.

## Slide 19
Table 20.2
Intel
8085 External Signals (page 2 of 2)

## Slide 20
Notes: These signals are the interface between the 8085
processor and the rest of the system (Figure 20.8).
The control unit is identified as having two components labeled (1) instruction
decoder and machine cycle encoding and (2) timing and control. A discussion
of the first component is deferred until the next section. The essence of the control
unit is the timing and control module. This module includes a clock and accepts as
inputs the current instruction and some external control signals. Its output consists
of control signals to the other components of the processor plus control signals to
the external system bus.
The timing of processor operations is synchronized by the clock and controlled
by the control unit with control signals. Each instruction cycle is divided into from
one to five machine cycles ; each machine cycle is in turn divided into from three to
five states. Each state lasts one clock cycle. During a state, the processor performs
one or a set of simultaneous micro-operations as determined by the control signals.
The number of machine cycles is fixed for a given instruction but varies
from one instruction to another. Machine cycles are defined to be equivalent to
bus accesses. Thus, the number of machine cycles for an instruction depends on
the number of times the processor must communicate with external devices. For
example, if an instruction consists of two 8-bit portions, then two machine cycles are
required to fetch the instruction. If that instruction involves a 1-byte memory or I/O
operation, then a third machine cycle is required for execution.

## Slide 21
Notes: Figure 20.9 gives an example of 8085 timing, showing the value of external
control signals. Of course, at the same time, the control unit generates internal control
signals that control internal data transfers. The diagram shows the instruction
cycle for an OUT instruction. Three machine cycles (M1 , M2 , M3 ) are needed. During
the first, the OUT instruction is fetched. The second machine cycle fetches the
second half of the instruction, which contains the number of the I/O device selected
for output. During the third cycle, the contents of the AC are written out to the
selected device over the data bus.
The Address Latch Enabled (Ale ) pulse signals the start of each machine
cycle from the control unit. The Ale pulse alerts external circuits. During timing
state T1 of machine cycle M1 , the control unit sets the IO/M signal to indicate that
this is a memory operation. Also, the control unit causes the contents of the PC
to be placed on the address bus (A15 through A8 ) and the address/data bus (AD7
through AD0 ). With the falling edge of the Ale pulse, the other modules on the
bus store the address.
During timing state T2 , the addressed memory module places the contents of the
addressed memory location on the address/data bus. The control unit sets the Read
Control (RD) signal to indicate a read, but it waits until T3 to copy the data from the
bus. This gives the memory module time to put the data on the bus and for the signal
levels to stabilize. The final state, T4 , is a bus idle state during which the processor
decodes the instruction. The remaining machine cycles proceed in a similar fashion.

## Slide 22
Table 20.3
A Decoder With
Four Inputs
and Sixteen Outputs
(Table can be found on page 725 in the textbook.)
Notes: Figure 20.4 depicts the control unit as we have so far discussed it. The key inputs are
the IR, the clock, flags, and control bus signals. In the case of the flags and control
bus signals, each individual bit typically has some meaning (e.g., overflow). The other
two inputs, however, are not directly useful to the control unit.
First consider the IR. The control unit makes use of the opcode and will perform
different actions (issue a different combination of control signals) for different
instructions. To simplify the control unit logic, there should be a unique logic input for
each opcode. This function can be performed by a decoder , which takes an encoded
input and produces a single output. In general, a decoder will have n binary inputs and
2n binary outputs. Each of the 2n different input patterns will activate a single unique
output. Table 20.3 is an example for n = 4. The decoder for a control unit will typically
have to be more complex than that, to account for variable-length opcodes. An
example of the digital logic used to implement a decoder is presented in Chapter 11.

## Slide 23
Notes: The clock portion of the control unit issues a repetitive sequence of pulses.
This is useful for measuring the duration of micro-operations. Essentially, the period
of the clock pulses must be long enough to allow the propagation of signals along
data paths and through processor circuitry. However, as we have seen, the control
unit emits different control signals at different time units within a single instruction
cycle. Thus, we would like a counter as input to the control unit, with a different
control signal being used for T1 ,T2 , and so forth. At the end of an instruction cycle,
the control unit must feed back to the counter to reinitialize it at T1 .
With these two refinements, the control unit can be depicted as in Figure 20.10.

## Slide 24: Summary
Micro-operations
  The fetch cycle
  The indirect cycle
  The interrupt cycle
  The execute cycle
  The instruction cycle
Control of the processor
  Functional requirements
  Control signals
  Internal processor organization
  The Intel 8085
Hardwired implementation
  Control unit inputs
  Control unit logic
Chapter 20
Control Unit Operation
Notes: Chapter 20 summary.